## Slide 1
NS-3 MANET ROUTING EXPERIMENT
Adaptive DSR Route Cache
Parameter sweep comparing mobility-scaled LinkCache timers against fixed DSR cache behavior
Fernando Molina Rodriguez Rajat Chaudhary
50
NODES
Random waypoint MANET
10
FLOWS
one-to-one UDP pairs
4
SWEEP POINTS
10%, 50%, 110%, 150%
200s
RUNTIME
one CSV row per second
Thesis
In high mobility, DSR should trust cached routes for less time. The experiment tests whether speed-scaled cache timers improve delivery.
Adaptive DSR route cache | 01

## Slide 2
PROBLEM
DSR cache reuse is valuable until mobility turns cached routes stale.
Adaptive DSR route cache | 02
Why the cache can hurt
DSR avoids repeated route discovery by keeping learned source routes and link state.
In RandomWaypoint mobility, a route that worked earlier can point through a now-broken link.
Long cache lifetimes can keep stale state alive long enough to drop packets before repair.
Adapt cache trust to movement
The experiment keeps the default MANET scenario and metrics, but computes cache timers from node speed before installing DSR.
Higher node speed -> shorter route and link stability timers

## Slide 3
FORMULA
A single mobility scale converts base cache timers into effective DSR values.
Adaptive DSR route cache | 03
adaptive_value = clamp(base_value * cache_reference_speed / node_speed, min_value, max_value)
Formula variables
base_value: original timer multiplied by the sweep percentage
cache_reference_speed: speed where base timers are preserved, 5 m/s
node_speed: scenario speed used for cache trust, 20 m/s
clamp: keeps timers inside configured safety bounds
This sweep used a 0.25 mobility scale
cache_reference_speed / node_speed = 5 / 20 = 0.25
Example: the 50% timeout starts at 150 s, then becomes clamp(150 * 0.25, 30, 300) = 37.5 s.
30-300s
ROUTECACHETIMEOUT
route lifetime bounds
2-25s
INITSTABILITY
new link confidence
10-120s
USEEXTENDS
successful-use extension

## Slide 4
IMPLEMENTATION
The adaptive values are computed before DSR is installed on the nodes.
Adaptive DSR route cache | 04
Command-line switches
adaptiveRouteCache
adaptiveLinkStability
cacheType
baseRouteCacheTimeout
baseInitStability
baseUseExtends
cacheReferenceSpeed
Config::SetDefault("ns3::dsr::DsrRouting::RouteCacheTimeout",
TimeValue(Seconds(m_effectiveRouteCacheTimeout)));
Config::SetDefault("ns3::dsr::DsrRouting::InitStability",
TimeValue(Seconds(m_effectiveInitStability)));
Config::SetDefault("ns3::dsr::DsrRouting::UseExtends",
TimeValue(Seconds(m_effectiveUseExtends)));
Placement matters: defaults must be set before dsrMain.Install(...) creates the routing objects.

## Slide 5
ADAPTIVE SWEEP
The 50% adaptive setting delivered the strongest packet count in this run.
Adaptive DSR route cache | 05
1261
BEST PACKET COUNT
50% adaptive run
3.228
AVG KBPS
full 200-second average
37.5s
EFFECTIVE TIMEOUT
50% base after scaling

## Slide 6
FIXED COMPARISON
Adaptive tuning beat fixed cache behavior at 50%, 110%, and 150%.
Adaptive DSR route cache | 06
+173
50% PACKET DELTA
adaptive vs fixed
+327
110% PACKET DELTA
largest improvement
-95
10% PACKET DELTA
low-end clamp loses

## Slide 7
TIME SERIES
Packet delivery starts after traffic begins and differs mainly during active seconds.
Adaptive DSR route cache | 07
How to read it
Rows are one simulated second. Traffic starts around 100 s, so the first half of each metrics file is intentionally zero. The comparisons use total packets and average kbps across the full 200 s for consistency with the default ns-3 example.

## Slide 8
TAKEAWAYS
Adaptive cache timing looks promising, but it needs seed and scenario sweeps next.
Adaptive DSR route cache | 08
What the experiment suggests
A moderate effective timeout outperformed both very short and long-lived cache assumptions.
The adaptive policy helped most when fixed DSR would otherwise keep stale cache state too long.
The 10% case exposes the impact of clamp bounds, so low-end tuning deserves separate attention.
Future work
Repeat runs across random seeds
Sweep cacheReferenceSpeed independently
Compare LinkCache and PathCache
Sweep node speed and node density
Track routing overhead alongside delivery
3/4
ADAPTIVE WINS
against fixed comparator
50%
BEST SWEEP POINT
1261 packets received
next
VARIANCE TESTING
multi-seed validation